## Slide 1: A-IoT : Work Package: Cabin Air Quality Monitoring August 2019
IISc Team
Indian Institute of Science, Bangalore

## Slide 2: Data generation architecture with Neural Network and Controller
Data generation model
Suffocation model for CO2
ECS Simulink model (TPH)
Controller
Neural network (detect root cause)
GUI
Flowrate(Fr),
Bleed- Recirculated Air ratio(X)
Passenger Count.
Anomalous conditions
CO2[1:6]
Humidity, Temperature, Pressure
Passenger count
Anomaly class
Set point
Fr,X
Fr
InfluxDB
Chronograf

## Slide 3
Scale,
X-axis:
1 unit = 1000 seconds
Y-axis :
1 unit = 1 units of signal
Time (Seconds)
Signals
Change in cabin parameters due to variation in flow rate
Fig. ECS parameter for Normal ventilation efficiency inside cabin
Fig. ECS parameter for Anomalous ventilation efficiency inside cabin
[Source: Simulink( MATLAB ECS)]

## Slide 4: Neural Network augmented Control system
Temperature | Pressure | Humidity | Passenger Count
Input Parameters For The Neural Network
Output Of The NN
Neural Network
CO2 across zones (1:6) | Rate of CO2 rise (1:6) | Deviation of zone from mean (1:6)
CLASS | DESCRIPTION | CONTROL ACTION
0 | No anomaly | NA
1 | Ventilation Efficiency | Increase Flowrate, Do not alter bleed-recirculation ratio (0.5).
2 | Internal Independent source | Maintain Flowrate, Increase bleed-recirculation ratio to 0.7
3 | External event | Maintain Flowrate, Increase bleed-recirculation ratio to 0.2
4 | Normal Conditions being restored | Maintain Flowrate, Increase bleed-recirculation ratio to 0.6
Class0 Class1 Class2 Class3 Class4
Confusion Matrix
The neural net has 22 input and 5 output neurons.
There are 4 hidden layers with 20,20,20 and 15 neurons sequentially.
A 70/30 training validation split is done over 332402 data frames.
The frame rate is 1/Sec and a total of 92 hrs of flight data is used for training and validation.

## Slide 5: Results for Class 1,2 and 3 anomalies for 75% occupancy

## Slide 6
Thank you
LOOKING FORWARD FOR YOUR SUPPORT