## Slide 1: A-IoT : Work Package: Cabin Air Quality Monitoring
IISc Team
Indian Institute of Science, Bangalore

## Slide 2: Possible control action implementation
Cabin & ECS Status
ECS
Intelligent Fast-loop Algos
CO2, Ozone, PM
Output
INPUT
(From data generation Model)
Decision for control action
Actuator :
Modify ECS parameters
Digital Controller
Y
N

## Slide 3: Factors affecting ECS
    Bleed Air ratio:
    It’s change affects the relative humidity and ozone level in the cabin, can act as a parameter .
    Flowrate / Ventilation Efficiency:
    Change in the flow rate/ Ventilation Efficiency will affect the Relative humidity levels inside the cabin.
    Cabin pressure will be effected due to variation in the Flowrate/Ventilation Efficiency.
Passenger aircraft cabin air quality: trends, effects, societal costs, proposals.
M.B. Hocking *, Department of Chemistry, University of Victoria, P.O. Box 3065 STN CSC, Victoria, BC, Canada V8W 3V6. Received 27 September 1999; ac0cepted 3 November 1999

## Slide 4: Factors considered for closed loop control action
Possible root cause for abnormal CO2 build up inside cabin, to implement closed loop control action :
    Change in ventilation.
    Ratio of Fresh/cabin air mixture
    CO2 concentration in bleed air due to external environment.

## Slide 5
Scale,
X-axis:
1 unit = 1000 seconds
Y-axis :
1 unit = 1 units of signal
Time (Seconds)
Signals
Change in cabin parameters due to variation in flow rate
Fig. ECS parameter for Normal ventilation efficiency inside cabin
Fig. ECS parameter for Anomalous ventilation efficiency inside cabin

## Slide 6: Simulation with ECS
GUI Simulate
ECS
CO2 & PM Equations
Data Generated
TICKStack automation
2018
GUI Simulate
Parameters Updating
( Flow rate, Ozone removal Efficiency, Pax)
CO2 & PM Equations
Data generated for each time sample
Input Intelligent aggregator
Controller
Controller Output
ECS
2019

## Slide 7: Data generation architecture with Neural Network and Controller.
Data generation model
Suffocation model for CO2
ECS Simulink model (TPH)
Controller
Neural network(detect root cause)
GUI
Flowrate(Fr),
Bleed- Recirculated Air ratio(X)
Passenger Count.
Anomalous conditions
CO2[1:6]
Humidity, Temperature, Pressure
Passenger count
Anomaly class
Set point
Fr,X
Fr

## Slide 8: Neural Network augmented Control system
Temperature | Pressure | Humidity | Passenger Count | CO2 across zones | Rate of rise of CO2 | Deviation of zone from mean | No anomaly | VE (flow rate) | Due To Independent Source | Due To Bleed | Class
Ta | Pa | Ha | Na | CO2[1:6] | dCO2[1:6] | CO2[1:6] - mean(CO2) |  |  |  |  | 0
Tb | Pb | Hb | Nb | CO2[1:6] | dCO2[1:6] | CO2[1:6] - mean(CO2) |  |  |  |  | 1
Tc | Pc | Hc | Nc | CO2[1:6] | dCO2[1:6] | CO2[1:6] - mean(CO2) |  |  |  |  | 2
Td | Pd | Hd | Nd | CO2[1:6] | dCO2[1:6] | CO2[1:6] - mean(CO2) |  |  |  |  | 3
Input parameters for the neural network
Output of the NN
The Neural Network is trained with data for different kinds of anomalies.
The Neural Network generates an output which is understood by the controller and a suitable control action is taken.

## Slide 9: Neural Network augmented Control system
Confusion Matrix
Model Evaluation Matrix
Class0 Class1 Class2 Class3 Class4

## Slide 10: Preliminary Results from neural network.
50% occupancy with Class 1 anomaly
100% occupancy with Class 1 anomaly

## Slide 11: Data set with different anomalous conditions
Class 1- Ventilation efficiency
Class 2 – Independent CO2 source
Class 3 – CO2 from bleed
Scale : Y axis – CO2 inppm. X axis- time in minutes
Scale : Y axis – RH (ratio). X axis- time in minutes

## Slide 12: Control actions to be implemented for various classes of anomalies
Class 1
  Caused due to poor ventilation.
  To be mitigated by increasing Flowrate.
Class 2
  Caused due to independent source
  To be mitigated by reducing recirculated air.
Class 3
  Caused by fuming events from bleed.
  To be mitigated by reducing bleed .

## Slide 13: Results: Class 1 anomaly
For 75% occupancy, without controller and neural network, CO2 levels rise upto 2300 ppm.
With Controller levels restricted to 1500 ppm

## Slide 14: Class 2 anomaly
For 50% occupancy, without controller and neural network, CO2 levels rise upto 3700 ppm.
With Controller levels restricted to 2900 ppm where bleed & recirculation ratio reduced to 0.7

## Slide 15: Class 3 anomaly
For 50% occupancy, without controller and neural network, CO2 levels rise upto 5400 ppm.
With Controller levels restricted to 4840 ppm and bleed: recirculation ratio of 0.2

## Slide 16
Work done:
  Generation and labelling datasets for different classes of anomalies.
  Training Neural nets for individual anomalies.
  Training the neural net using the complete dataset.
  Linking the data generation model with the neural net and controller for real time anomaly detection and control.
  Closing the loop by control action implementation and visualisations by integrating TICK stack.
Tasks underway:
Optimizing neural network

## Slide 17
Thank you
LOOKING FORWARD FOR YOUR SUPPORT